## Slide 1: Stream Sediment Load Monitoring in Morehead, Kentucky
Presented by Kristopher Krolikowski
Department of Physics, Earth Science, and Space Systems Engineering

## Slide 2: Introduction
All streams throughout the world carry varying amounts of sediment as they flow.
Sediment loads and concentrations in streams are directly related to several issues, with the most notable being flood concerns.
Stream systems that experience a large and rapid influx of sediment may have new or significantly worse flooding events.

## Slide 3: Introduction
  Any large-scale removal of upstream vegetation will cause increased sediment load in a stream.
  Construction projects and logging are the two most common causes of sediment load increases.
  Increased load can result in new bed forms or other sedimentation events which may cause channel misdirection or blockage.
  Either case can increase flood risk.
Notes: Morehead has seen significant floods in the past, and remains a flood prone area to this day, even with stable stream systems. Now that large-scale logging is occurring upstream of one of Morehead’s major stream systems, the flooding in the area has the potential to worsen.

## Slide 4: Thesis Premise
Flooding is a concern in the downtown Morehead area.
Perception that increased sedimentation due to increased logging will exacerbate flood risk.
This thesis was designed to monitor and assess sedimentation and flood risk along logging impacted and unimpacted portions of Oxley Branch and Town Branch.
Notes: My goal here is to monitor and compare stream systems in Morehead that have ben directly impacted by logging operations for increased sediment concentrations. This in turn will give us a good indication on whether or not upstream logging has an impact on flooding downstream.

## Slide 5: Geologic Background of Morehead, Kentucky
Morehead is located at the Western edge of the Appalachian Plateau in an inverted topography of steeply sloping ridges and valleys produced when streams dissected the Pleistocene Peneplain.
Bedrock geology in the study area consists of variably thick shale, sandstone, and siltstone beds forming the Nancy and Cowbell Members of the Borden Formation.
Thick, unstable colluvium and alluvium deposits blanket the lower slopes and the valley floor.
Denuded slopes are exceptionally prone to erosion.

## Slide 6
Morehead
Notes: Here is a Geologic map of Morehead. As you can see, the entire city area as well as the study area surface geology consists almost entirely of colluvium and alluvium sediment deposits. Most of your underlying rock beds you will find in the area will consist of sandstones, siltstones, or shales.

## Slide 7: Study Area
To Interstate 64
Study Area
Oxley Branch Site
Evans Branch Site
Town Branch Site
N
Adron-Doran University Center
St. Claire Regional Hospital
Morehead
U.S. 60
U.S. 32
Notes: This is a satellite image map of Morehead for better orientation. Each monitoring site is labeled here, as well as St. Claire Regional Hospital, the Adron-Doran University Center (ADUC), US 60, and US 32 for reference.

## Slide 8: Monitoring Site: Oxley Branch
Notes: This is a close up image of the Oxley Branch site. The red square is the primary area of focus to include the stream itself, and the blue arrow is the direction of water flow.

## Slide 9: Monitoring Site: Town Branch
Notes: Same as last slide, only for Town Branch.

## Slide 10: Control Site: Evans Branch
Baird Music Hall
Battson-Oates Drive
Notes: Here is the Evans Branch control site. This is actually on campus right beside Baird Music Hall.

## Slide 11: Stream Data Collection
Stream cross-sections were each hand-measured with a measuring tape and meter stick to determine channel width, depth, as well as the depth of water at high flow.
Water velocities were calculated using the Float-Area Method.
Stream discharges were calculated following the USGS Discharge Measurement Standard.
Notes: For the Float-Area method, floating material is timed from a start point to a finish point along a predetermined distance down the stream. Multiple attempts are required in order to average the results for better precision. I used popcorn as the floating material because it is highly visible and floats well in water. The recorded time is then multiplied by the distance that was traveled to get velocity in m/s.
All measurements were done using metric units to maintain a set standard throughout the project.

## Slide 12: Stream Discharge Calculations (USGS Standard)
Image Source: https://www.usgs.gov/special-topic/water-science-school/science/how-streamflow-measured?qt-science_center_objects=0#qt-science_center_objects
Cross-sectional area of water = depth of water x width of channel
Velocity of water = change in distance / change in time
Notes: This diagram shows how to use the USGS Standard to find streamflow, or discharge.
Discharge is the amount of flowing water that travels through the stream in a certain amount of time. It is quantified in units of cubic meters per second.

## Slide 13: Stream Data
Site Name: | Oxley Branch | Town Branch | Evans Branch
Stream Width (cm): | 196.60 cm | 124.46 cm | 554.74 cm
Stream Depth (cm): | 117.35 cm | 28.04 cm | 141.73 cm
Depth of Water (cm): | 39.62 cm | 4.44 cm | 27.43 cm
Water Velocity (m/s): | 0.63 m/s | 1.29 m/s | 0.22 m/s
Cross-Sectional Area of Water (m2): | 0.78 m2 | 0.055 m2 | 1.52 m2
Stream Discharge (m3/s): | 0.49 m3/s | 0.07 m3/s | 0.33 m3/s
Notes: This table shows all of the general stream data for each monitoring site that I collected and calculated. Discharges and velocities were recorded and calculated at a period of high-flow (either immediately after a hard rain or during consistent snow melt).

## Slide 14: Sediment Data Collection
6 water samples in total, 2 at each site, were collected during high flow.
The samples were collected using glass bottles placed directly into the flowing stream during a time of high flow.
All 6 bottled samples were taken to the lab for further evaluation.
In the lab, each sample was weighed and then poured slowly through a filter to collect only the sediment left behind.
This filter was then dried and weighed to find the gross weight of the sediment.
Further calculations were made using the newly found sediment weights to determine concentrations for each stream.
Notes: The weights of sediment for each stream were averaged and set to units of grams.
Sediment concentrations were calculated in terms of Parts Per Million and Milligrams of sediment per Liter of water.

## Slide 15: Sediment Data
Site Name: | Oxley Branch | Town Branch | Evans Branch
Average Weight of Sediment (grams): | 0.103g | 0.025g | 0.0045g
Sediment Concentration (PPM): | 266.93 PPM | 68.52 PPM | 11.34 PPM
Sediment Concentration (mg/L): | 320.31 mg/L | 71.26 mg/L | 11.45 mg/L
Notes: Oxley Branch has experienced consistent, heavy logging for the past year leading up to the sample collection time.
Town Branch has seen heavy logging in the past, but little logging has occurred in past year.
Evans Branch (Control Site) has seen no serious logging for at least 5 years.
As we can see here, the sites that active logging is occurring upstream or previous logging has occurred clearly show an increase in sediment concentrations compared to a location where no logging has occurred recently.
Evans Branch and Oxley Branch have similar discharges, but vastly different sediment concentrations, which confirms that outside interference is occurring.

## Slide 16: Conclusion
The sediment data collected clearly indicates that upstream logging has a direct impact on stream sediment concentrations.
Oxley Branch (Active Logging) has almost 30 times the amount of sediment concentration that Evans Branch (Control) does.
Town Branch (Past Logging) has just over 6 times the sediment concentration that Evans Branch (Control) does.
If the sediment concentrations in Oxley Branch go unchecked for much longer, the already bad flooding along its path could worsen.
Notes: The cause of the influx of sediment on Oxley Branch is the removal of vegetation upstream, which causes sediments to travel with groundwater freely following precipitation events.
Town Branch represents a stream returning to its original sediment concentrations. Since it hasn’t seen logging in the past year, but it has within the last 5, it still has increased concentrations compared to Evans Branch, but nothing like that of Oxley.
If safe logging practices are used to mitigate sediment runoff from the logging sites, flooding in the down stream areas could become less of a concern.